## Slide 1
Linux on ESP32-S3 (N16R8)
Build, flash and boot nommu Linux from a Linux PC
Steps, memory, cores, functionality and limits

## Slide 2
What runs where
Linux PC (build host)
Builds toolchain, kernel, root filesystem
Flashes images over USB with esptool
Serial terminal to see the console
Not needed once flashed
ESP32-S3 (target)
Runs bootloader and Linux kernel
Runs BusyBox shell and programs
Wi-Fi through ESP-Hosted firmware
Everything executes on the chip
Linux runs 100% on the ESP32-S3. The PC only builds, flashes and shows the console.

## Slide 3
Build steps (on the PC)
Install host packages (build-essential, bison, flex, cmake, etc.)
Clone github.com/jcmvbkbc/esp32-linux-build
Apply workarounds for new tools (GCC 13, CMake policy)
Run ./rebuild-esp32s3-linux-wifi.sh (about 1 to 2 hours)
Script builds: Xtensa toolchain, bootloader, Linux kernel, Buildroot rootfs, Wi-Fi firmware
Check images: xipImage, rootfs.cramfs, etc.jffs2, bootloader, partition table

## Slide 4
Problems we hit and fixes
GCC 15 broke GMP
Error: could not find a working compiler
Cause: GCC 15 uses C23; old GMP fails
Fix: install gcc-13, put it first in PATH
export PATH=$HOME/oldgcc:$PATH
CMake 4 broke host-lzo
Error: compatibility with CMake < 3.5 removed
Cause: old package, new CMake
Fix: set a policy minimum
export CMAKE_POLICY_VERSION_MINIMUM=3.5
Result: toolchain and kernel built; Buildroot rootfs was the last step.

## Slide 5
Flash and boot
Hold BOOT, tap RESET to enter download mode
Flash with esptool.py --chip esp32s3 write_flash, using offsets from the build output
Open console: picocom -b 115200 /dev/ttyACM0
Press RESET: bootloader, kernel messages, then Buildroot login (root)
If no output: try the other USB port, check baud, confirm octal PSRAM setting

## Slide 6
Memory and flash usage
Flash: 16 MB chip
This build is the devkit_c1_8m config
Uses an 8 MB layout
About half the flash is unused
Using all 16 MB needs a custom partition layout
RAM: 8 MB PSRAM
Octal PSRAM is the Linux main memory
Internal SRAM serves bootloader and firmware
Very small for Linux, keep programs light
Execute in place
Kernel (xipImage) runs straight from flash
rootfs.cramfs is read-only, stored in flash
etc.jffs2 holds writable config
Exact partition sizes come from the build output; check the partition table to confirm.

## Slide 7
CPU cores
ESP32-S3: dual-core Xtensa LX7, up to 240 MHz
No MMU, so nommu Linux: no virtual memory, no memory protection
Wi-Fi runs as separate ESP-Hosted firmware on the same chip
Exact core split depends on the port version; verify after boot with: cat /proc/cpuinfo
Performance is far below a Raspberry Pi; suited to learning and small tasks

## Slide 8
Functionality and limits
What works
Serial console and BusyBox shell
Basic Linux tools and filesystem
Wi-Fi networking via ESP-Hosted
Programs built for nommu (FDPIC)
Limits
No fork(); only nommu-built programs run
Very small RAM, slow boot
Wi-Fi setup is the fiddliest part
Hardware drivers (GPIO, I2C) depend on the port

## Slide 9
Summary
Linux runs fully on the ESP32-S3; the PC is only for build and flash
Uses jcmvbkbc nommu port: Xtensa toolchain, kernel, Buildroot rootfs
Our build targets an 8 MB flash layout, so half of the 16 MB is unused
8 MB octal PSRAM is Linux RAM; dual cores at up to 240 MHz
Two build fixes: GCC 13 and CMake policy 3.5
Next: finish rootfs build, flash, boot to shell